CSCI 3511 Hardware/Software Interface
Final Team Project

Alex Barkov, Jon Petraglia, Nic Young
Fall 2012

Project Purpose:
The purpose of this project is to use the PIC 32 Robotic Starter Kit, using the Cerebot 32MX4 PIC32MX460F512L in conjunction with the PmodLS1 infrared light detector and the IR Proximity Sensor, to navigate a maze using the IR proximity sensors ability to detect IR input to control the direction. The project demonstrates our ability to:
- ability to identify, formulate, and solve engineering problems;
- ability to communicate effectively;
- ability to use the techniques, skills, and modern engineering tools necessary for engineering practice;
- ability to design software and/or hardware to meet desired needs.
Common Project Requirements:
1. The robot shall navigate a maze from a designated start point to a designated finish point.
2. The robot shall be physically placed at the designate start point by the operator.
3. The robot shall use the PmodLS1infrared light detector in conjunction with two IR Proximity Sensors to detect infrared light originating from the operator.
4. The robot shall activate the appropriate motors in order to move in the direction of the IR light source detected.
5. The maze shall be marked out on a tile floor using duct tape or similar adhesive material.
6. The robot shall will not start detecting IR until Button 2 has been pressed on the robot.
7. The maze shall be constructed so that the navigating robot must turn left and right to be able to successfully navigate the maze.

Project Design
Program Files
File	Description
Config.h	This header contains declarations used to configure the project based on the target platform
Main.c	This program is a reference design for the Digilent Line Sensor Robotic Development Kit (RDK-Line) with the Cerebot 32MX4 Microcontroller board. It uses two timers to drive two motors with output compare modules.
Main.d	Config file for main.c
MtrCtrl.d	Config file for MtrCtrl.c
MtrCtrl.h	This module contains declarations and definitions for controlling the robot motors using a combination of pulse width modulation and pulse width timing of the feedback signals provided by the DC motors.
MtrCtrl.c	This module contains declarations and definitions for controlling the robot motors using a combination of pulse width modulation and pulse width timing of the feedback signals provided by the DC motors.

Main Public Interface:
Function	Description
Timer5Handler()	Interrupt service routine for Timer 5 interrupt. Timer 5 / is used to perform software debouncing of the on-board buttons. It is also used as a time base for updating the on-board LEDs and the Pmod8LD LEDs at a regular interval.
ChangeNotice_Handler()	Interrupt service routine for all four light sensors via the change notice interrupt handler. Each time a change in sensor state occurs, this routine is called. It assess current sensor state and determines new duty cycles for both motors to correctly follow a line.
Main()	Main program module. Performs basic board initialization and then enters the main program loop.
DeviceInit()	Initializes on chip peripheral devices to the default state.
AppInit()	Performs application specific initialization. Sets devices and global variables for application.
Wait_ms()	Will wait for specified number of milliseconds. Using a word variable allows for delays up to 65.535 seconds. The value in the for statement may need to be altered depending on how your compiler translates this code into AVR assembly. In assembly, it is possible to generate exact delay values by counting the number of clock cycles your loop takes to execute. When writing code in C, the compiler interprets the code, and translates it into assembly. This process is notoriously inefficient and may vary between different versions of AVR Studio and WinAVR GCC. A handy method of calibrating the delay loop is to write a short program that toggles an LED on and off once per second using this function and using a watch to time how long it is actually taking to complete.

Function Call Graph

Software Development Environment
- Operating Systems: Linux x86_64
- IDE: MPLABx v. 1.41
Hardware Configuration Bit Settings
Bit	Value	Desription
ICESEL	ICS_PGx2	ICE/ICD Comm Channel Select
BWP	OFF	Boot Flash Write Protect
CP	OFF	Code Protect
FNOSC	PRIPLL	Oscillator Selection
FSOSCEN	OFF	Secondary Oscillator Enable
IESO	OFF	Internal/External Switch-over
POSCMOD	HS	Primary Oscillator
OSCIOFNC	OFF	CLKO Enable
FPBDIV	DIV_8	Peripheral Clock divisor
FCKSM	CSDCMD	Clock Switching & Fail Safe Clock Monitor
WDTPS	PS1	Watchdog Timer Postscale
FWDTEN	OFF	Watchdog Timer
FPLLIDIV	DIV_2	PLL Input Divider
FPLLMUL	MUL_16	PLL Multiplier
UPLLIDIV	DIV_2	USB PLL Input Divider
UPLLEN	OFF	USB PLL Enabled
FPLLODIV	DIV_1	PLL Output Divider
PWP	OFF	Program Flash Write Protect
DEBUG	OFF	Debugger Enable/Disable

Physical Layout Plan
For the physical layout we have cordoned off a 3x3 meter space. We will then use duct tape to create the maze that the robot will navigate. We will indicate the starting postion and ending position of the maze with distinguishable duct tape.
Robot Setup and Pre-Conditions
1. The robot must be pre-programmed with the maze navigation program.
2. The robot must start at the same starting position indicated by the piece of duct tape.
3. The testing space must be a a level hard wood or tile floor.
4. The IR sensors must be aligned correctly to allow for the robot to turn in the correct direction when IR is detected.
5. The PModLS1infr must be securely connected to the robot.
Results
Error Control
Source Code Attachments